## Slide 1: HIP Programming Course
AMD GPU Architecture Overview

## Slide 2: Introduction
So far, we have considered the GPU as a set of consumable resources (memory and compute) with a given functionality dictated by the API and the user application. From this point of view, these are things that we know:
A kernel is a piece of code that is run on the GPU by many instances (work-items or threads) concurrently.
Ideally, each work-item works with its own different elements of data. Also, variables/registers created/used by a work-item are accessible only to the work-item.
Work-items are organized in waves (wavefronts or warps) of 64 work-items each.
Work-items in a wavefront run in lockstep mode; all of them execute the same operation at the same time (like following the same program counter). – Conceptually, we can think of a wavefront as a CPU-thread running vector operations of length 64.
Wavefronts are grouped in workgroups or thread-groups of maximum 1024 work-items each.
Conceptually, the work-items in a workgroup can be arranged in a 3D array of dimensions blockDim.x by blockDim.y by blockDim.z.
Similarly, the workgroups can be arranged in a grid of gridDim.x by gridDim.y by gridDim.z groups.
The size and shape of the grid and its workgroups is defined by software when launching the kernels.

## Slide 3: Introduction

## Slide 4: Introduction
All the work-items in a workgroup can access a common local memory (Local Data Share or LDS), and can be synchronized via specific API instructions.
Work-items from different workgroups cannot be synchronized and only share access to the Global memory on the GPU which is orders of magnitude slower than LDS.
The normal workflow of GPU accelerated computations is:
  Transfer input data from CPU (the host) to GPU (the device)
  Kernel execution on the GPU to process data
  Transfer result data back to CPU
Launching a kernel is a non-blocking operation from the host perspective. Data transfers could be blocking (synchronous) or non-blocking (asynchronous).
When using asynchronous data transfers, we need a mechanism to ensure the CPU is not launching a kernel before the input data is ready on the GPU, or starting the transfer of the results before the kernel execution is completed. The use of streams provides such mechanism.

## Slide 5: Introduction
A stream is a queue of tasks or commands (kernels or data transfers) on the GPU. All the commands in the same stream are executed in the order they were queued, but the execution of commands from different streams could overlap.
Modern GPUs have many resources to execute kernels from different streams concurrently and, normally, two different data transfer engines, one for each direction. This allows transfer host-to-device and device-to-host to run concurrently as well.
The use of events provides additional functionality to synchronize commands from different streams.
Now we want to see the GPU as a series of hardware blocks and sub-blocks that interact with each other to enable the described functionality of the GPU resources.

## Slide 6: Contents
The purpose of this presentation is to provide an overview of the AMD GPU architecture and to lay some foundations for better understanding advanced programming tools and optimization techniques that take advantage of hardware mechanisms with direct impact in performance.
  Chip versioning, architecture families, consumer products
          Prehistory, the GCN architecture, RDNA vs CDNA architectures
  GCN / CDNA architecture overview
          6 levels of zooming: from functional blocks to specific hardware components
  By the numbers
          GCN / CDNA flagship products in the numbers

## Slide 7: 1. Chip versioning, Architecture families, Consumer products
In 2006, AMD acquired ATI (Array Technologies Inc.), a Canadian based semiconductor company specialized in Graphics Processing Units (GPUs)
In 2010-2011 there is a rebranding of the GPU products (the name ATI is removed from the cards), and a redesign of the GPU architecture is completed with the introduction of the Graphics Core Next (GCN) architecture. GCN is at the base of our modern GPUs today.
With GCN, AMD also adopted the ‘gfx’ chip versioning
  gfxXYZ X: mayor version, Y: minor version and Z: revision
  Major versions indicate non-backward compatible ISA
  Minor versions and revisions indicate, extensions to the ISA, or configuration changes that allow the compiler to generate more optimal code, for example.
In 2019 with the fifth generation of the GCN architecture (gfx9 chip version), AMD started to manufacture chips with 7nm transistor size technology
At this point, to ensure scalability of future chips, GCN architecture was overhauled originating:
  the new RDNA architecture (gfx10 chip version), specialized in graphics
  CDNA architecture (still gfx9 chip version) for compute. Based on GCN but completely removing the graphics stack from the hardware
gfx10 and gfx9 chips have non-fully compatible ISAs and, as CDNA has no graphics stack,
there are important differences in how RDNA and CDNA architectures operate

## Slide 8: 1. Chip versioning, Architecture families, Consumer products
Architecture | Chip version | Transistor size | Code name | Product example | Year
GCN | gfx600 | 28nm | Tahiti | Radeon HD 7970 | 2011
GCN2 | gfx701 | 28nm | Hawaii | Radeon R9 290 | 2013
GCN3 | gfx803 | 28nm | Fiji | Radeon Instinct MI8 | 2016
GCN4 | gfx803 | 14nm | Polaris | Radeon RX 580 | 2017
GCN5 | gfx900 | 14nm | Vega10 | Radeon Instinct MI25 | 2017
GCN5 | gfx906 | 7nm | Vega20 | Radeon Instinct MI60 | 2019
RDNA | gfx1010 | 7nm | Navi10 | Radeon RX 5700XT | 2019
RDNA2 | gfx1030 | 7nm | Navi21 | Radeon RX 6900XT | 2020
CDNA | gfx908 | 7nm | MI100 | Radeon Instinct MI100 | 2020
CDNA2 | gfx90a | 6nm | MI200 / Hayabusa | Radeon Instinct MI250 | 2021

## Slide 9: Contents
The purpose of this presentation is to provide an overview of the AMD GPU architecture and to lay some foundations for better understanding advanced programming tools and optimization techniques that take advantage of hardware mechanisms with direct impact in performance.
  Chip versioning, architecture families, consumer products
          Prehistory, the GCN architecture, RDNA vs CDNA architectures
  GCN / CDNA architecture overview
          6 levels of zooming: from functional blocks to specific hardware components
  By the numbers
          GCN/CDNA flagship products in the numbers

## Slide 10: 2. GCN / CDNA Architecture overview (Index)
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 11: 2.0 The functional blocks
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 12
Compute block
Memory block
Control
block

## Slide 13
Compute block
Memory block
Control
block
Control block
Process commands from the host app (mem transfer, synch or kernel dispatch)
Supervises/facilitates the execution of the command in either the compute or mem block; Host only initiates the command
It may signal back to host once the command is completed
Host could:
  be waiting for signal
  get Interrupted by the signal
  forget about signal
Collaborates with OS for other functions (graphics, power, security)

## Slide 14
Compute block
Memory block
Control
block
Compute block
Programable by users
It is there to process the data of the memory block
Reads program (kernel instructions) from host or mem block
Organizes wavefronts (work-items) to execute instructions exploiting parallelism at different levels
  Can handle multiple wavefronts from different work-groups at once
  Can execute different types of instructions at once
  In a vector instruction, it works with multiple data items at once

## Slide 15
Compute block
Memory block
Control
block
Memory block
Physically separated from host memory
Has combination of data and program
Interacts with:
  Host memory (PCIe bus)
  Memory blocks from other GPUs (PCIe bus / interconnect)
  Itself and the compute block (internal memory hierarchy, on-chip)

## Slide 16: 2.1 Heart of functional blocks
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 17
Compute block
Memory block
Control
block

## Slide 18
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Control
block
Compute block

## Slide 19
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Control
block
Compute block
Device Memory
Dynamic RAM
32GiB – 128GiB in total
48 bits virtual mem space (TBs of mem space)
High bandwidth in the order of TB/s (0.6 – 1.6)
Off-chip but on the GPU card
It is, in general, the memory accessible to the outside world
Internal mem buffers
Cache like SRAM tech
Order(s) of magnitude faster than device mem
Depends on level and functionality; the closer to the registers the faster:
  Auxiliary and translation caches
  Level 2 and 1 streaming caches (pathway from CU to device mem)
  Data shares (user managed cache)

## Slide 20
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Control
block
Compute block

## Slide 21
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Control
block
Compute block
CP

## Slide 22
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Control
block
Compute block
Command processor (CP)
Main controller; implements the scheduling engine (ScE)
It reads a location in host mem where the app write the commands
Decodes commands and starts work in the other GPU components. Facilitates the work:
  Set arguments in registers
  Flush caches
  Create and distribute workgroups
  Starts mem transfers
At the end, it writes back to another location in host mem to signal completion
CP

## Slide 23
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Control
block
Compute block
CP

## Slide 24
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)

## Slide 25
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
Compute unit (CU) 1/2
GPU core made by a series of compute units
Replicated hardware components organized in a hierarchy
A single CU enables vector operations (64 work-items). All work-items share resources of the CU.
Multiple CUs sharing resources form a shader array.
Multiple shader arrays share resources in a shader engine (SE)
Compute unit (CU) 2/2
Multiple shader engines provide the compute power required by the CP to process commands
The purpose of the design is modularity and replication:
  configuration of the hardware can change easily for different products
  Functionality of a CU is replicated; need to see inside a single SE -> array -> CU

## Slide 26: 2.2 Hardware specialization
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)

## Slide 27
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)

## Slide 28
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs

## Slide 29
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
Command processor fetcher (CPF)
Fetches and decodes commands from the host (kernel launch, mem transfer or synchronization)
Delegates the work to the specialized unit
  CPC to dispatch a kernel
  DMA for a mem transfer
Ready to fetch the next command

## Slide 30
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
Direct mem access engine (DMA)
Receives location of source and recipient, size, etc.
  Host to device
  Device to host
  Device to device
Copies and stores chunks of data at a time
Only one mem transfer per DMA at a time
There are multiple DMAs (at least 2 to take advantage of bidirectional PCIe)
No direct access to CU data
Once a transfer is done, the DMA informs the host

## Slide 31
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Direct mem access engine (DMA)
Receives location of source and recipient, size, etc.
  Host to device
  Device to host
  Device to device
Copies and stores chunks of data at a time
Only one mem transfer per DMA at a time
There are multiple DMAs (at least 2 to take advantage of bidirectional PCIe)
No direct access to CU data
Once a transfer is done, the DMA informs the host

## Slide 32
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Memory controllers
Several controllers. One per channel
Each channel covers a fixed range of memory address
Normally interleaved with 128 stride
Translation caches
ATC for the CPU space:
  4-way associative, 64 sets in 2 banks
  Total of 2 x 64 x 4 x 64B = 32 KiB (4,096 translations)
GPUVM for the GPU space:
  8-way associative, 256 sets in 2 banks
  Total of 2 x 256 x 8 x 64B = 256 KiB (32,768 translations)
Unified translation cache (UTC):
  Fully associative
  Total of 4 KiB (512 translations)

## Slide 33
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers

## Slide 34
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ

## Slide 35
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
Command processor compute (CPC)
Receives the info about the kernel(s):
  Grid shape and sizes,
  Pointer to the kernel code,
  Arguments, etc.
Organizes the workgroups and dispatch them, one at a time, to the SPIs in a round-robin fashion
Multi-engine; can process many kernel launches at a time
Once a kernel is done executing the CPC informs the host
Interacts with the caches and registers (housekeeping: flush data to device memory)

## Slide 36
CPC
G0
G0
G4
CU0
CU1
CU2
CU3
SPI0
G1
G1
G5
CU0
CU1
CU2
CU3
SPI1
G2
G2
CU0
CU1
CU2
CU3
SPI2
G3
CU0
CU1
CU2
CU3
SPI3
K0
Kernel 0: 3 groups
of 4 waves
Kernel 1: 6 groups
of 2 waves
K1

## Slide 37
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
Command processor compute (CPC)
Receives the info about the kernel(s):
  Grid shape and sizes,
  Pointer to the kernel code,
  Arguments, etc.
Organizes the workgroups and dispatch them, one at a time, to the SPIs in a round-robin fashion
Multi-engine; can process many kernel launches at a time
Once a kernel is done executing the CPC informs the host
Interacts with the caches and registers (housekeeping: flush data to device memory)

## Slide 38
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
Shader processor input (SPI) 1/2
Further divides the workgroups into wavefronts and dispatch them, one at a time, to the SQs
Prepare the CU to execute the wavefront (set registers with arguments, etc.)
All the SPIs cooperate to dispatch workgroups in order (baton-passing)
SPI launching group 0 passes the baton to SPI launching group 1 after the first wavefront is dispatched
Once the SPI started dispatching waves from a workgroup, it will continue until it is done
All waves from a group must go to the same CU. In the presence of many workgroups, the SPI dispatches their waves into different CUs in a round-robin fashion.

## Slide 39
CPC
G0
G0
G4
CU0
CU1
CU2
CU3
SPI0
G1
G1
G5
CU0
CU1
CU2
CU3
SPI1
G2
G2
CU0
CU1
CU2
CU3
SPI2
G3
CU0
CU1
CU2
CU3
SPI3
K0
G0W0
G0W1
G1W0
G2W0
G1W1
G2W1
G3W0
G3W1
Kernel 0: 3 groups
of 4 waves
Kernel 1: 6 groups
of 2 waves
K1
X
X
X
X
X
X
X
G0W0
G0W1
G0W2
G0W3
G1W0
G1W1
G1W2
G1W3
G2W0
G2W1
G2W2
G2W3
G4W0
G4W1
G5W0
G5W1

## Slide 40
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
Shader processor input (SPI) 2/2
The SPIs have a “scoreboard” (called the Crawler) that keeps track of wavefronts in the SE
An entry indicates: Kernel_x, group_y, wavefront_z
Space for (32 x # of CUs in SE) entries in the crawler
Entries are removed from the Crawler when the wavefront is done, and the scoreboard collapses
There is a special entry: kernel_x EOP indicating the end of kernel_x
When the EOP is the oldest entry alive in the SPIs they let know the CPC the kernel is done

## Slide 41
CPC
CU0
CU1
CU2
CU3
SPI0
CU0
CU1
CU2
CU3
SPI1
CU0
CU1
CU2
CU3
SPI2
CU0
CU1
CU2
CU3
SPI3
G0W0
G0W1
G1W0
G2W0
G1W1
G2W1
G3W0
G3W1
G0W0
G0W1
G0W2
G0W3
G1W0
G1W1
G1W2
G1W3
G2W0
G2W1
G2W2
G2W3
G4W0
G4W1
G5W0
G5W1
G0W0
G0W1
G0W0
G0W1
G0W2
G0W3
EOP
G4W0
G4W1
EOP
SPI0 crawler

## Slide 42
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ

## Slide 43
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
GWS / GDS

## Slide 44
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
GWS / GDS
Global Data Share (GDS)
Similar to the shared memory (LDS) in functionality but way smaller
4 KiB shared by all the CUs in all the SEs
No high-level ease to use (look at the ISA)
Rather called Global Wave Sync (GWS)

## Slide 45
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
GWS / GDS
Sequencer (SQ)
Receives the list of wavefronts from the SPI
It fetches up to 8 instructions (32 bytes) of one of the wavefronts at a time
Then it dispatches an instruction of possibly multiple wavefronts every cycle
  A wavefront can have only one instruction in execution
  There could be instructions of different wavefronts on flight at the same time if they don’t use the same execution units in the CU

## Slide 46
Shader Arrays
CUs
SEs
CP
Device Memory
HBM DRAM
(off chip)
SRAM memory buffers hierarchy
(on chip)
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
SPI
SQ
GWS / GDS

## Slide 47
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
SQ

## Slide 48
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
SQ
Types of instructions
Branch: the entire wavefront will jump to another part of the code (e.g. device function call)
Scalar-ALU: when all work-items will see/use the same result. Only one arithmetic operation is executed -only one ALU is needed (e.g. calculating a common offset)
  Vector-ALU to be discussed later
Memory operations: scalar (wavefront-wide access), or vector (each work-item access its own data)
Data share memory operations
All instructions are issued at a wavefront level (all work-items run in lock-step)

## Slide 49
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
SQ

## Slide 50: 2.3 Consumable resources (the idea of Occupancy)
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 51
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
SQ

## Slide 52
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ

## Slide 53
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
General Purpose Registers (GPRs)
GPRs are 4 bytes wide. Two consecutive registers are used for 64-bit values
SGPRs holds the same value for all the work-items in wavefront. A VGPR, on the other hand, is 64 registers wide.
There are 800 SGPRs available for the wavefronts associated to each SIMD. A single wavefront could allocate up to 128 of them.
There are 256 VGPRs available for the wavefronts associated to each SIMD. A single wavefront could allocate all of them.
In total, the register files sizes are:
  4 x 800 x 4B = 12.5 KiB (scalar)
  4 x 256 x 64 x 4B = 256 KiB (vector)

## Slide 54
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ

## Slide 55
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
LDS

## Slide 56
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
LDS
Local Data Share (LDS)
Fast memory with embedded logic for atomic operations to support inter-lane interaction
Very close to the registers (user managed cache)
No connection to memory outside the compute units
32 banks of 512 4-bytes entries for a total of 32 x 512 x 4B = 64KiB

## Slide 57: Occupancy
Defined as the ratio of actual wavefronts that will live in a CU to the theoretical maximum number of wavefronts that supports the hardware.
It could indicate under-utilization of the resources, which could lead to lower performance.
The max number of wavefronts depends on the pool of resources that we are looking at: registers, LDS, wavefront slots, total number of wavefronts in workgroup etc.
The smallest ratio is the one limiting the occupancy.
Note: high occupancy (close to 1) does not necessarily mean good performance; low occupancy does not necessarily mean bad performance… balance is key!

## Slide 58: Occupancy
Some factors impacting occupancy: #1 scalar registers
The max number of wavefronts associated to a SIMD is 10 (more on this later)
The max number of SGPRs that a wavefront could use is 128 out of 800
SGPRs / wave | Waves / SIMD | Max waves / SIMD | Ratio
128 | 6 | 10 | 6/10 (60%)
100 | 8 | 10 | 8/10 (80%)
< 80 | 10 | 10 | 10/10 (100%)

## Slide 59: Occupancy
Some factors impacting occupancy: #2 vector registers
The max number of wavefronts associated to a SIMD is 10 (more on this later)
The max number of VGPRs that a wavefront could use is 256 out of 256
VGPRs / wave | Waves / SIMD | Max waves / SIMD | Ratio
24 | 10 | 10 | 10/10 (100%)
64 | 4 | 10 | 4/10 (40%)
> 128 | 1 | 10 | 1/10 (10%)

## Slide 60: Occupancy
Some factors impacting occupancy: #3 LDS
LDS is consumed per workgroup!!!
The max number of wavefronts per CU is 40 (more on this later)
  If groups have a single wave, there could be up to 40 workgroups per CU
  If groups have more than one wave (2 to 16), there could be at most 16 workgroups per CU
Total LDS per CU is 64KB
LDS / group | Groups / CU | Waves / group | Waves / CU | Max waves / CU | Ratio
64 KiB | 1 | 4 | 4 | 40 | 4/40 (10%)
64 KiB | 1 | 16 | 16 | 40 | 16/40 (40%)
8 KiB | 8 | 3 | 24 | 40 | 24/40 (60%)
8 KiB | 8 | 5 | 40 | 40 | 40/40 (100%)

## Slide 61
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
LDS

## Slide 62
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
LDS
SL1
TCP

## Slide 63
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
LDS
SL1
TCP
Texture Cache per Processor (TCP)
Read/Write L1 Cache
Replicated with each CU to ensure full scalability of the shader system
Fully associative. 4 banks of 64 lines; 1 line is 64 bytes
Total of 4 x 64 x 64B = 16 KiB
Sequencer Data Cache (SL1)
Similar to TCP. Used to cache scalar values (all work-items see the same value)
Shared by all the CUs in a shader array
16 KiB in total.
4-way associative. 1-4 banks of 16-32 sets per bank.

## Slide 64: 2.4 The SIMD engines (Data parallelism)
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 65
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
SQ
LDS
SL1
TCP

## Slide 66
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP

## Slide 67
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
Fetch arbiter and Instruction Buffers (IB)
There are 4 pools in which the waves dispatched by the SPI could be organized
There is space in each pool to hold the information of up to 10 wavefronts: workgroup ID, process ID, pointers to register file, program counter, pointer to the kernel code etc.
Up to 40 waves simultaneously on the CU
Up to 16 process in a CU simultaneously
Every cycle, the fetch arbiter fetches 32 bytes of instructions from the earliest serviced wavefront out the 40 and put them in the corresponding IB
These instructions are cached in the SQC

## Slide 68
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
Fetch arbiter and Instruction Buffers (IB)
There are 4 pools in which the waves dispatched by the SPI could be organized
There is space in each pool to hold the information of up to 10 wavefronts: workgroup ID, process ID, pointers to register file, program counter, pointer to the kernel code etc.
Up to 40 waves simultaneously on the CU
Up to 16 process in a CU simultaneously
Every cycle, the fetch arbiter fetches 32 bytes of instructions from the earliest serviced wavefront out the 40 and put them in the corresponding IB
These instructions are cached in the SQC

## Slide 69
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
Sequencer Cache (SQC)
Shared by all the CUs in a shader array
32 KiB in total.
4-way associative. 1-4 banks of 32-64 sets per bank.
Fetch arbiter and Instruction Buffers (IB)
There are 4 pools in which the waves dispatched by the SPI could be organized
There is space in each pool to hold the information of up to 10 wavefronts: workgroup ID, process ID, pointers to register file, program counter, pointer to the kernel code etc.
Up to 40 waves simultaneously on the CU
Up to 16 process in a CU simultaneously
Every cycle, the fetch arbiter fetches 32 bytes of instructions from the earliest serviced wavefront out the 40 and put them in the corresponding IB
These instructions are cached in the SQC

## Slide 70
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
Dispatch Arbiter
Every cycle switches pools in a round-robin fashion
It selects, from the 10 waves in the pool, those that are ready to run an instruction
A wavefront can run if it is not running anything yet, and if it’s going to use a free execution unit
  In each cycle, up to 6 waves can start running an instruction
  For the same wave to run 2 instructions in a row, it must wait at least 4 cycles
SQC

## Slide 71
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC

## Slide 72
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3

## Slide 73
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
SIMDs (Vector ALUs)
4 x 16-lanes SIMDs, each one associated to one and only one IB (pool of wavefronts)
As vector instruction is 64 wide (64 work-items in the wavefront), but there is only 16 ALUs, it takes 4 cycles for a SIMD to complete it
  The same 4 cycles it takes for the arbiter to have an opportunity to dispatch another vector instruction to that SIMD, i.e. no stall time!!
The design allows hardware replication and running vector operations from multiple wavefronts in parallel

## Slide 74: Peak performance - Instructions per cycle
IB_0
VALU_0
Cycle 0
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
IB_1
VALU_1
IB_2
VALU_2
IB_3
VALU_3
W0
W1
W2
W3
W4
W5
W0
0-15
W0
16-31
W0
32-47
W0
48-63
W4
0-15
W1
0-15
W1
16-31
W1
32-47
W1
48-63
W2
0-15
W2
16-31
W2
32-47
W3
0-15
W3
16-31
W6
W7
W0
W1

## Slide 75: Peak performance - Instructions per cycle
IB_0
VALU_0
Cycle 0
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
IB_1
VALU_1
IB_2
VALU_2
IB_3
VALU_3
W0
W1
W2
W3
W4
W5
W0
0-15
W0
16-31
W0
32-47
W0
48-63
W4
0-15
W4
16-31
W4
32-47
W4
48-63
W1
0-15
W1
16-31
W1
32-47
W1
48-63
W5
0-15
W5
16-31
W5
32-47
W5
48-63
W2
0-15
W2
16-31
W2
32-47
W2
48-63
W3
0-15
W3
16-31
W3
32-47
W3
48-63
W6
W7
W6
0-15
W6
16-31
W6
32-47
W6
48-63
W7
0-15
W7
16-31
W7
32-47
Theoretical peak performance:
MI100 has 120 CUs with 4 SIMDs with 16 ALUs each
120 x 4 x 16 flops / cycle = 7,680 flops / cycle
The clock freq is 1502 MHz… so,
7,680 flops/cycle x 1,502,000,000 cycles/sec = 11.5 Tflops/sec

## Slide 76: Peak performance - Instructions per cycle
Instructions per cycle (IPC)
Distinction between IPC at a wavefront level vs work-item level
Every cycle a wavefront is completed; the 64 work-items did something. IPC = 1
However, not all the work-items will commit their result. IPC is not always 64 at the work-item level!!
  There is an Execution Mask Register associated to each wave
  If the k-th bit is set, then the k-th work-item execute and commit its result
  This is how branching at work-item level is handled…
i = thread_id;
A[i] = i + 1;
i = thread_id;
j = i % 64;
if(j < 32)
A[i] = i + 1;
else
A[i] = i - i;
Wavefront IPC = 1
Work-item IPC = 64
Wavefront IPC = 1
Work-item IPC = 64/2 = 32

## Slide 77
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3

## Slide 78
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs

## Slide 79
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
Texture Cache per Channel (TCC) 1/2
Read/write L2 cache
Cache on the memory side; attached to the controllers on each channel (16 to 32 channels)
Total of 64 KiB – 256 KiB per TCC
16-way associative. 2-4 banks, 64-128 sets per bank.
The TCCs see all the TCPs in the CUs; operations in TCC are atomic
Texture Cache per Channel (TCC) 2/2
Efficiency and coherency achieved with common mechanisms:
  Two CUs can write in parallel to L2 if they will touch different parts of the cache line (false sharing)
  CUs send a Dirty Mask using bits to indicate which bytes in the line should be updated (1 bit for every 4 bytes)
  The L1 (TCP) is write-through. Every change in a TCP block is also written in TCC

## Slide 80: 2.5 Scheduling work
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 81
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs

## Slide 82: HSA / DMA Queues and signals
Streams and events are software mechanisms. Queues and signals are the hardware counterpart.
A queue is a user-visible contiguous region on memory where an application writes “packets” that the GPU will interpret as commands (kernel launch, mem transfer, synchronizations)
A signal is a location in memory where the GPU writes and integer value
  Non-zero value = signal not completed
  Zero = signal completed
User launches an app that uses GPU  the driver helps create/assign a queue/signals
From there, all the interaction CPU-GPU is done by writing and reading to/from these memory locations
Stream 0
Stream 1
Stream 2
Stream 3
Stream n
…
…
Queue 0
Queue 1
Queue 2
Queue 3
Queue m
HIP runtime (ROCr)

## Slide 83: HSA / DMA Queues and signals
Two types of queues:
  HSA (Heterogenous system architecture)
    For compute commands
    Contains AQL (Architected queuing language) packets
  DMA (Direct memory access)
    For memory transfer commands
    Contains PM4 packets
AQL packets are 64 bytes. PM4 packets vary in length.
AQL packets don’t change regardless of the target device. PM4 packets are vendor/hardware specific.
AQL is very simple, essentially 2 packets: kernel dispatch and barrier
PM4 language is more convoluted; many different packets (for graphics, video, etc.) For mem transfers.
PM4 and AQL understand signals and can work with the same signals.
In general, the packets have 3 parts:
  Header. First bytes. Info like the type of packet. Other relevant info like scope of fences, barrier bits, etc.
  Body. Depends on the type of packet (variable length in case of PM4 packets). Contains info like: number of groups and sizes, pointer to code, pointer to the data to transfer, size of the transfer, signals to wait for, etc.
  Completion Signal. Pointer to the signal to decrement at completion.

## Slide 84: HSA / DMA Queues and signals
The queues could have many producers but only one consumer: the device.
Queues have a Write pointer (where the software will start writing packets) and a Read pointer (where the software finished reading packets)
Pointers travel the queue in a circular manner (modulus).
The read pointer is always chasing the write pointer. When write = read, the queue is empty (all packets have been read). When write = read + # of entries, the queue is full (no packet has been read).
All queues have a doorbell associated. When someone writes a packet it also write the index of the last packet in the doorbell. This wakes up the CP and ask it to start reading packets at the read pointer position.
HSA queue
…
Producer 1: 2 packets
Producer 2: 3 packets
Producer 3: 1 packets
doorbell

## Slide 85: HSA / DMA Queues and signals
The queues could have many producers but only one consumer: the device.
Queues have a Write pointer (where the software will start writing packets) and a Read pointer (where the software finished reading packets)
Pointers travel the queue in a circular manner (modulus).
The read pointer is always chasing the write pointer. When write = read, the queue is empty (all packets have been read). When write = read + # of entries, the queue is full (no packet has been read).
All queues have a doorbell associated. When someone writes a packet it also write the index of the last packet in the doorbell. This wakes up the CP and ask it to start reading packets at the read pointer position.
HSA queue
…
Producer 1: 2 packets
Producer 2: 3 packets
Producer 3: 1 packets
doorbell
0

## Slide 86: HSA / DMA Queues and signals
The queues could have many producers but only one consumer: the device.
Queues have a Write pointer (where the software will start writing packets) and a Read pointer (where the software finished reading packets)
Pointers travel the queue in a circular manner (modulus).
The read pointer is always chasing the write pointer. When write = read, the queue is empty (all packets have been read). When write = read + # of entries, the queue is full (no packet has been read).
All queues have a doorbell associated. When someone writes a packet it also write the index of the last packet in the doorbell. This wakes up the CP and ask it to start reading packets at the read pointer position.
HSA queue
…
Producer 1: 2 packets
Producer 2: 3 packets
Producer 3: 1 packets
doorbell
2

## Slide 87: HSA / DMA Queues and signals
The queues could have many producers but only one consumer: the device.
Queues have a Write pointer (where the software will start writing packets) and a Read pointer (where the software finished reading packets)
Pointers travel the queue in a circular manner (modulus).
The read pointer is always chasing the write pointer. When write = read, the queue is empty (all packets have been read). When write = read + # of entries, the queue is full (no packet has been read).
All queues have a doorbell associated. When someone writes a packet it also write the index of the last packet in the doorbell. This wakes up the CP and ask it to start reading packets at the read pointer position.
HSA queue
…
Producer 1: 2 packets
Producer 2: 3 packets
Producer 3: 1 packets
doorbell
2

## Slide 88: HSA / DMA Queues and signals
The queues could have many producers but only one consumer: the device.
Queues have a Write pointer (where the software will start writing packets) and a Read pointer (where the software finished reading packets)
Pointers travel the queue in a circular manner (modulus).
The read pointer is always chasing the write pointer. When write = read, the queue is empty (all packets have been read). When write = read + # of entries, the queue is full (no packet has been read).
All queues have a doorbell associated. When someone writes a packet it also write the index of the last packet in the doorbell. This wakes up the CP and ask it to start reading packets at the read pointer position.
HSA queue
…
Producer 1: 2 packets
Producer 2: 3 packets
Producer 3: 1 packets
doorbell
5

## Slide 89: HSA / DMA Queues and signals
hipLaunchKernelGGL(kernelA,…,stream1,…);
hipMemcpyAsync(…,hipMemcpyDeviceToHost,stream1);
hipLaunchKernelGGL(kernelB,…,stream2,…);
hipLaunchKernelGGL(kernelC,…,stream3,…);
hipStreamSynchronize(stream1);
some_cpu_function();
hipDeviceSynchronize();
Hip runtime
HSA queue 1
HSA queue 2
DMA queue 1
Host
Host
Barrier_AND
Signals

## Slide 90
Shader Arrays
CUs
SEs
SPI
CPC
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs

## Slide 91
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs

## Slide 92
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
Asynchronous Compute Engines (ACEs)
4 engines (four hardware threads). Also called scheduling pipes.
8 software threads per pipe for a total of 32 threads.
Each thread could service one HSA queue at a time.
Queue_0  pipe_0 thread_0
Queue_1  pipe_1 thread_0
Queue_2  pipe_2 thread_0
Queue_3  pipe_3 thread_0
Queue_4  pipe_0 thread_1 …
A packet in queue_4 cannot be processed until the packet in queue_0 is done, or after 10ms.
There is a SPI crawler per pipe.

## Slide 93: 2.6 Other hardware components
Control functional-block
RLC - Runtime Low power Controller
SMU -System Management Unit
SPI – Shader Pipe Input per SE
SQ - Sequencer per CU
  IB - 4 x Instruction buffers
  Fetch/dispatch arbiter
Control and comms Network
  SMN - System Management Network
  GPU Core internal network
CP - Command processor (ScE)
  CPG - CP for graphics
  DMA - Direct Memory Access engines
  CPF - CP Fetcher
    HSA Queues
  CPC - CP for Compute
    ACEs - Asynchronous Compute Engines (ME)
Compute functional-block
Compute Units are organized in Shader Arrays
Shader Arrays are organized in Shader Engines
CU - Compute Unit(s)
  Branching and msg unit
  Memory decode unit
  DS decode unit
  Scalar ALU
    SGPRs - Scalar registers
  Vector ALU
    VGPRs – Vector registers
    4 x 16 lines SIMDs
Memory functional-block
Off-chip DRAM Device memory
  Memory banks or channels (DRAM controller + TCC block)
On-chip mem buffers hierarchy (SRAM technologies)
  Auxiliary buffers
  Virtual address caches
    ATC/GPUVM - Virtual address translation for CPU/GPU
    UTC - Unified address translation
  Data shares
    GWS - Global Wave Sync (also called GDS)
    LDS - Local Data Share
  Streaming caches
    TCP - Texture Cache per processor (L1)
    SQC/SL1 - Sequencer instruction/data cache(s)
    TCC - Texture Cache per Channel (L2)

## Slide 94
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs

## Slide 95
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
SMU
RLC

## Slide 96
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
SMU
RLC
Runtime Low-power Controller (RLC)
Its purpose is to ensure the best performance per watt
Power management with clock gating and power gating
Management in a per CU basis and for the entire GPU
Works in conjunction with the SMU

## Slide 97
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
SMU
RLC
System Management Unit (SMU)
More general-purpose piece of hardware. Deals with operative system interactions
Assists in:
  Central power management
  Context switching (when there is graphics stack)
  Security, virtualization
Runtime Low-power Controller (RLC)
Its purpose is to ensure the best performance per watt
Power management with clock gating and power gating
Management in a per CU basis and for the entire GPU
Works in conjunction with the SMU

## Slide 98
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
SMU
RLC

## Slide 99
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
SMU
RLC
AUX
MEM

## Slide 100
Shader Arrays
CUs
SEs
SPI
CPF
DMAs
ATC / GPUVM
UTC
TCCs
DRAM
Controllers
Device Memory
HBM DRAM
(off chip)
GWS / GDS
Branch
SALU
SGPR
Mem
Decode
LDS dec
Fetch arbiter
Dispatch arbiter
IB_0
IB_1
IB_2
IB_3
VGPR
VGPR
VGPR
VGPR
LDS
SL1
TCP
SQC
VALU_0
VALU_1
VALU_2
VALU_3
TCCs
ACEs
SMU
RLC
AUX
MEM
Control and communication networks
System management network (SMN)
  At SOC level
  Scalable control fabric (SCF)
  Scalable data fabric (SDF)
Internal GPU core network
  Communications hubs and crossbars

## Slide 101: Contents
The purpose of this presentation is to provide an overview of the AMD GPU architecture and to lay some foundations for better understanding advanced programming tools and optimization techniques that take advantage of hardware mechanisms with direct impact in performance.
  Chip versioning, architecture families, consumer products
          Prehistory, the GCN architecture, RDNA vs CDNA architectures
  GCN / CDNA architecture overview
          6 levels of zooming: from functional blocks to specific hardware components
  By the numbers
          GCN/CDNA flagship products in the numbers

## Slide 102: 3. By the numbers

## Slide 104
DISCLAIMER
The information contained herein is for informational purposes only, and is subject to change without notice. While every precaution has been taken in the preparation of this document, it may contain technical inaccuracies, omissions and typographical errors, and AMD is under no obligation to update or otherwise correct this information. Advanced Micro Devices, Inc. makes no representations or warranties with respect to the accuracy or completeness of the contents of this document, and assumes no liability of any kind, including the implied warranties of noninfringement, merchantability or fitness for particular purposes, with respect to the operation or use of AMD hardware, software or other products described herein. No license, including implied or arising by estoppel, to any intellectual property rights is granted by this document. Terms and limitations applicable to the purchase or use of AMD’s products are as set forth in a signed agreement between the parties or in AMD's Standard Terms and Conditions of Sale. GD-18
©2023 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo, Radeon, Radeon Instinct, and combinations thereof are trademarks of Advanced Micro Devices, Inc. PCIe is a registered trademark of PCI-SIG Corporation. Other product names used in this publication are for identification purposes only and may be trademarks of their respective companies.